PART 1 GENERAL

1.01 SCOPE

A. 	Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architects/engineers drawings, in new or retrofit installations of potable water structures.

1.02 SUBMITTALS

A. 	Submit to joint manufacturer drawings indicating location of joint and configurations.

B. 	Manufacturers printed literature and installation instructions.

PART 2 PRODUCT

2.01 DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to:  ± 2" [ ± 50 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B. 	All details and connections are factory fabricated by means of vulcanization.

C. 	Joint material is to be AquaLINE as supplied by SITURA INC., 1-888-474-8872, batch certified to NSF-61.

PART 3 EXECUTION

3.01 INSTALLATION

A. 	Install all components of the system in accordance with the manufacturers most recent printed instructions. The system is to be wholly encapsulated in a two component, high viscosity, epoxy resin. Epoxy resin shall be certified for use in potable water.

B. 	The epoxy resin is applied to the substrate and the bottom surface of the AquaLINE. The AquaLINE is embedded in to it, by pressing. The top surface of the AquaLINE is then covered by the epoxy resin and allowed to dry. The joint shall not obstruct water flow across its surface and forms a continuous monolithic waterproof barrier

3.02 PRECAUTIONS

- The applicator must observe the open pot time of the epoxy resin manufacturer

END OF SECTION