PART 1 GENERAL

  - SCOPE

- Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architects/engineers drawings, in new or retrofit installations.

  - SUBMITTALS

A. 	Submit to joint manufacturer drawings indicating location of joint and configurations.

B. 	Manufacturer's printed literature and installation instructions.

PART 2 PRODUCT

2.01 DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to: ± 1" [ ± 25 mm] / ± 2" [ ± 50 mm] / ± 10" [± 240 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B.	All details and connections are factory fabricated by means of vulcanization.

C.	Joint material is to be FlamLINE [20], [40], [240] as supplied by SITURA INC., (888) 474-8872.

PART 3 EXECUTION

3.01 INSTALLATION

- Install all components of the system in accordance with the manufacturer's instructions. The system is to be wholly encapsulated between the plies of the modified bitumen membrane in a roofing/waterproofing by torching. The joint can be protected by means of an overlap membrane mopped or torched to one side of the joint as per manufacturer's instructions.

- Slit the modified bitumen base ply with a knife along the joint gap. Refer to the manufacturer's instructions for the preparations and torching of the FlamLINE. Torch the prepared FlamLINE to the substrate, making sure that the FlamLINE is firmly and uniformly set, without voids, into the liquefied asphalt. Torching is carried out by the liquefaction of the modified bitumen base sheet and the FlamLINE rolled into it. Flame can be directed at the FlamLINE material. At all times observe the modified bitumen manufacturer's recommendations and safety instructions. The FlamLINE must be completely encapsulated in the hot asphalt/bitumen and a bitumen bead visible along FlamLINE salvage edge.

- Torch the modified bitumen stripping plies smooth, free from air pockets, wrinkles, fish mouths, or tears. When torching, direct the flame away from the FlamLINE gland material, use the torch and flop technique. Install each stripping ply; shingle lap fashion, onto the FlamLINE firmly and uniformly, without voids. At all times observe the modified bitumen manufacturer's recommendations. The FlamLINE must be completely encapsulated in the melted bitumen and a bitumen bead visible along the FlamLINE salvage edge

3.02 PROTECTION

A	Additional protection to the FlamLINE joint is optional but can be provided by attaching a modified bitumen sheet to one side of the FlamLINE joint. This is achieved by either mopping or torching the modified bitumen sheet to the already installed modified bitumen cap ply.

END OF SECTION