PART 1 GENERAL

1.01	SCOPE

A.	Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architects/engineers drawings, in new or retrofit installations.

1.02 SUBMITTALS

A.	Submit to joint manufacturer drawings indicating location of joint and configuration.

B.	Manufacturer’s printed literature and installation instructions.

PART 2 PRODUCTS

2.01	DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to: ± 1" [ ± 25 mm] / ± 2" [ ± 50 mm] / ± 10" [± 240 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B.	All details and connections are factory fabricated by means of vulcanization.

C.	Joint material is to be RedLINE [20], [20G], [40], [40G], [240] as supplied by SITURA INC., 1-888-474-8872.

PART 3 EXECUTION

3.01 	INSTALLATION

A.	Install all components of the system in accordance with the manufacturer’s most recent printed instructions.

B.	RedLINE is installed typically in an asphaltic based medium. Apply the base coat of the asphaltic medium directly to the substrate and embed the RedLINE waterproof expansion joint material, and making sure that the bottom polyester fleece is in full contact with the hot asphalt. Press the RedLINE material into the hot asphalt material.

C.	Spread an even coat of asphalt on the top surface of the RedLINE expansion joint ensuring the top white polyester fleece is completely covered and strip in felt plys. The system is to be wholly encapsulated between plies in an [asphalt/bitumen] compatible roofing/waterproofing system with flood coat (mopping is acceptable) of [asphalt/bitumen]. The joint shall not obstruct water flow across its surface and forms a continuous monolithic waterproof barrier.

3.02 PRECAUTIONS

A.	Always lay the RedLINE expansion joint material only in lengths of 10 feet [3 m] or less to allow for contact with the hot asphalt material. Do not lay the RedLINE in cold asphalt.

3.03 PROTECTION

A.	The joint can be protected by means of an overlap membrane mopped to one side of the joint as per manufacturer’s instructions.

END OF SECTION