PART 1 GENERAL

1.01 SCOPE

A. 	Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architects/engineers drawings, in new or retrofit installations.

1.02 SUBMITTALS

A. 	Submit to joint manufacturer drawings indicating location of joint and configuration.

B. 	Manufacturers printed literature and installation instructions.

PART 2 PRODUCT

2.01 DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to: ± 2" [ ± 50 mm] / ± 6" [± 150 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B. 	All details and connections are factory fabricated by means of vulcanization.

C. 	Joint material is to be RedLINE [40], [240] as supplied by SITURA INC., 1-888-474-8872.

PART 3 EXECUTION

3.01 INSTALLATION

A.	Install all components of the system in accordance with the manufacturers most recent printed instructions.

B. 	The system is to be wholly encapsulated between plies in a coal tar pitch roofing/waterproofing system with flood coat of coal tar pitch.

C. 	Install a base ply set in mastic over the joint gap to prevent the flow of pitch into the joint. Provide for ply envelopes to prevent the migration of pitch into the joint cavity

D. 	Apply the base coat of the coal tar pitch directly to the substrate and embed the RedLINE waterproof expansion joint material, and making sure that the bottom polyester fleece is in full contact with the hot pitch. Press the RedLINE material into the hot pitch material.

E. 	Spread an even coat of pitch on the top surface of the RedLINE expansion joint ensuring the top white polyester fleece is completely covered and strip in felt plies. The system is to be wholly encapsulated between plies. The joint shall not obstruct water flow across its surface and forms a continuous monolithic waterproof barrier.

F. 	Add two ply polyester reinforced sheet, embedded in Coal Tar Pitch on top of the RedLINE as a protection if required.

3.02 PRECAUTIONS

- Always lay the RedLINE expansion joint material only in lengths of 10 feet [3 m] or less to allow for contact with the hot pitch. Do not lay the RedLINE in cold pitch.

END OF SECTION