PART 1 GENERAL

1.01 SCOPE

A. 	Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architects/engineers drawings, in new or retrofit installations.

1.02 SUBMITTALS

A.	Submit to joint manufacturer drawings indicating location of joint and configurations.

B. 	Manufacturer’s printed literature and installation instructions.

PART 2 PRODUCT

2.01 DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to: ± 1" [ ± 25 mm] / ± 2" [ ± 50 mm] / ± 10" [± 250 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B.	All details and connections are factory fabricated by means of vulcanization.

C.	Joint material is to be RedLINE [20], [20G], [40], [40G], [240] as supplied by SITURA INC., 1-888-474-8872.

PART 3 EXECUTION

3.01 INSTALLATION

A. 	Install all components of the system in accordance with the manufacturer’s most recent printed instructions.

B.	Encapsulate the RedLINE material in the surface coating of the spray polyurethane foam, alternatively if the setting time of the foam is long, embed the RedLINE in the base coat of the polyurethane foam roof.

C.	The top surface fleece of the RedLINE must be covered by the coating applied to the polyurethane roof or embedded in the polyurethane base coat. The joint shall not obstruct water flow across its surface and forms a continuous monolithic waterproof barrier.

D.	Consult the manufacturer for specific application procedures.

END OF SECTION