PART 1 GENERAL

1.01 SCOPE

A.	Provide factory fabricated elastomeric expansion waterproofing joint, to prevent the penetration of water at control, expansion or building joints as indicated on architect’s/engineer’s drawings, in new or retrofit installations.

1.02 SUBMITTALS

A.	Submit to joint manufacturer drawings indicating location of joint and configurations.

B. 	Manufacturer’s printed literature and installation instructions.

PART 2 PRODUCT

2.01 DESCRIPTION

A. 	Provide flat, vulcanized waterproofing joint integral with the waterproofing membrane to accommodate movements up to: ± 1" [ ± 25 mm] / ± 2" [ ± 50 mm] / ± 4" [ ± 100 mm] / ± 10" [ ± 250 mm] capable of 500% elongation at - 40 °F [- 40 °C] across its length and at all vulcanized points.

B. 	All details and connections are factory fabricated by means of vulcanization.

C. 	Joint material is to be FlamLINE [20], [40], [100], [240] as supplied by SITURA INC., 1-888-474-8872.

PART 3 EXECUTION

3.01 INSTALLATION

A. 	Install all components of the system in accordance with the manufacturer’s most recent printed instructions. The system is to be wholly encapsulated in a two component, high viscosity, epoxy resin.

B.	The epoxy resin is applied to the substrate and the bottom surface of the yellow FlamLINE flange is embedded in to it, by pressing. The top surface of the flange is then similarly covered by the epoxy resin and allowed to dry. Do not cover the black gland with epoxy. The joint shall not obstruct water flow across its surface and forms a continuous monolithic waterproof barrier.

3.02 PRECAUTIONS

A.	The applicator must observe the open pot time of the epoxy resin manufacturer.

3.03 PROTECTION

A.	The joint material can be protected by means of a light gauge metal cover, to match external finishes, if required.

END OF SECTION